## Slide 1
AAVISHKAR 2026–27
Maharashtra State Inter University Research Convention
What do four sensors miss?
Establishing the observability and reliability limits of low-cost plantar sensor arrays for wearable gait characterisation
CATEGORY Engineering & Technology
LEVEL UG
CODE NO.
01 / THE PROBLEM
A whole pressure field. Four small sampling areas.
Pressure map
Sparse sensors
Unobserved area
sample
outside discs
50 mm
50 mm
50 mm
Dense reference
4 assumed discs
No direct measurement
R2 / SPATIAL COVERAGE
COMPLETED SUBSET ANALYSIS
3.55%
Barefoot (BF)
Range 2.76–4.25%
2.18%
Sneaker (ST)
Range 1.66–2.81%
Mean loaded area observed.
Ranges show participant variation,
not confidence intervals.
0
129.1 kPa
Stance-mean pressure
Same right-foot example: participant 002, BF/W1, step 1.
5 mm/cell, 12.7 mm discs. Toes up; medial side left.
The four-sensor model observes
only a small fraction of loaded area.
02 / HOW WE MEASURED IT
BF
ST
Dataset
StepUP-P150
trials
Step selection
First eligible steps
steps
Pressure grid
Side + pitch verified
grids
Sensor layout
Fixed circular discs
masks
Overlap analysis
Fractional cell area
scores
Aggregation
Equal subject weight
means
Results
Conditions separate
12
Participants
IDs 002–013
2
Conditions
BF + ST, preferred speed
576
Steps
12 / foot / condition
5
Layout models
4, 6, 8, 13, 16 sensors
03 / LAYOUT COMPARISON
Mean loaded area observed (%)
Chart: 
| 4 | 6 | 8 | 13 | 16
Barefoot (BF) | 3.5493 | 5.0317 | 6.0573 | 8.9903 | 11.617
Sneaker (ST) | 2.1811 | 3.2992 | 3.8341 | 6.1136 | 8.2018
Sensor count in each layout model
Count and position both change.
R1 / ENDURANCE
to be measured
repeated load
FSR specimen
Planned loading schematic
Compare calibration before and
after repeated loading.
R3 / MEASUREMENT VALIDITY
to be measured
Drift checks
VALID
Report
DEGRADED
Suppress
INVALID
Recalibrate
Proposed gate
Test with aged sensors from R1.
Firmware integration pending.
CONCLUSION
Limited spatial coverage is the finding. Floor-pressure data do not validate in-shoe performance.
Next: endurance testing, then validity-gate testing. Reliability remains to be measured.
Contact ≥2% of frame peak; fractional overlap; equal participant weighting. Assumed layout geometry, not measured Niva sensor positions. R2 protocol 799f322; run_20260912T161228Z.
Sources: Larracy et al., Scientific Data (2025), doi:10.1038/s41597-025-05792-1. StepUP-P150, doi:10.20383/103.01285. Planned experiments: Niva research framework.
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285.
Visual-first revision. All three footprint panels use the same individual BF example and physical scale. Third panel subtracts exact circular discs from the mean pressure display as a geometric illustration, not an extra outcome. R1 and R3 drawings are proposed test schematics without result data. Full research title retained beneath the display question; confirm registration wording/code before print.
Transparent Niva compact vector logo adapted from user-provided brand artwork, with increased prominence.