## Slide 1
AAVISHKAR 2026–27
Maharashtra State Inter University Research Convention
What do four sensors miss?
Spatial observability of low-cost plantar sensor arrays
Full research title
Establishing the observability and reliability limits of low-cost plantar sensor arrays for wearable gait
characterisation
CATEGORY
Engineering & Technology
LEVEL
UG
CODE NO.
Notes: Display title and scientific subtitle shortened at the user’s request. The full framework title remains visible for registration compliance. Confirm registered wording and fill the code number. R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285.
Niva compact logo vector trace from user-supplied 03_compact_lockup_on_light.png. Transparent flat-colour adaptation, with outlined lettering and a light wordmark on the dark closing slide.

## Slide 2
NIVA / AAVISHKAR 2026–27
02
PROBLEM STATEMENT
Missing pressure limits gait characterisation
Engineering & Technology / UG
Niva research instrument
sample
Dense reference
Four local samples
A load shift can occur between
sensors
Pressure outside the discs has no direct
measurement channel.
Engineering impact
Whole-foot load distribution and
centre-of-pressure estimates then depend
on assumptions about the missing field.
Same BF right-foot example: participant 002, W1, step 1. Discs use the assumed 12.7 mm geometry.
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285. This is a measurement-geometry argument, not evidence of a particular gait error or event-detection failure. Reference diagram: stance-mean pressure, 5 mm pitch. Four local signals do not directly observe pressure outside the model discs.

## Slide 3
NIVA / AAVISHKAR 2026–27
03
RESEARCH GAP + OUR CONTRIBUTION
Characterisation is the research contribution
Engineering & Technology / UG
Niva research instrument
GAP FOR THIS INSTRUMENT
OUR CONTRIBUTION
Spatial coverage
Unknown coverage of the assumed sparse
layouts.
R2 / completed
Reproducible overlap analysis on a fixed public-data
subset.
Endurance
Sensitivity change under repeated load is
unmeasured.
R1 / planned
A sensitivity-versus-cycles study with repeated
calibration.
Measurement validity
Loss of validity has no validated detection rule.
R3 / proposed
Test a reporting gate with deliberately aged sensors.
The insole is the instrument. The completed contribution is the R2 subset analysis.
Notes: Research framework sections 2, 3 and 7 establish the project framing. Gap wording is scoped to this instrument, not a claim that no related published work exists. R1 and R3 contributions are planned. R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285.

## Slide 4
NIVA / AAVISHKAR 2026–27
04
AIM & OBJECTIVES
Define the instrument’s measurement limits
Engineering & Technology / UG
Niva research instrument
R2
COMPLETED SUBSET
Spatial coverage
Quantify area and load
overlap across five fixed
layout models.
Output: participant means and
ranges
R1
PLANNED
Endurance
Track sensitivity and zero
offset against repeated load
cycles.
Output: degradation curve
to be measured
R3
PLANNED
Measurement validity
Test drift detection using
sensors aged in R1.
Output: detection rate, false alarms,
latency
to be measured
Notes: Objectives define outputs rather than implying validation. R1/R3 have no measured outcomes. Sources: research framework objectives and planned experiments. R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285.

## Slide 5
NIVA / AAVISHKAR 2026–27
05
METHODOLOGY
R2 analysis workflow
Engineering & Technology / UG
Niva research instrument
Dataset
StepUP-P150
trials
Selection
Eligible
footsteps
grids
Sensor-layout
modelling
Fixed circular discs
masks
Overlap
analysis
Fractional cell area
scores
Aggregation
Equal participant
weight
means
BF
ST
Results
BF and ST
separately
Aggregation order
Frames
Steps
Each foot
Participant
Group
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285. Diagram stages are schematic. Sensor modelling verifies side and pitch and mirrors left-foot columns. 12.7 mm discs at preserved 5 mm pitch. Contact threshold >=2% of frame maximum. Fixed 32 by 32 fractional-overlap subgrid. All loaded frames retained, including zero sparse signal. Aggregate frames into step means, then steps within side, sides within participant and equal-weight participants within condition.

## Slide 6
NIVA / AAVISHKAR 2026–27
06
SYSTEM / MODEL STATUS
Implementation and validation status
Engineering & Technology / UG
Niva research instrument
IMPLEMENTED/ANALYZED
R2 computational pipeline
Selection, layout modelling and overlap
analysis run on archived pressure data.
Existing acquisition firmware
ESP32 with four FSR402 channels, MPU6050
and heel piezo.
PENDING
Integrate niva_signal.h fixes, then verify acquisition
and calibration.
PROPOSED / VALIDITY GATE
Drift checks
Baseline drift
Re-zero divergence
Channel consistency
VALID
Report
DEGRADED
Suppress
INVALID
Recalibrate
check outcome
PENDING: gate integration and R3 tests.
Detection performance: to be measured.
Notes: Implementation describes repository code, not verified hardware measurement. niva.ino still uses STREAM_INTERVAL_MS=50 and +/-2g conversion at inspection. niva_signal.h is not included in niva.ino. Research framework defines the proposed validity checks. R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285.

## Slide 7
NIVA / AAVISHKAR 2026–27
07
EXPERIMENTAL SETUP
How the 576 footsteps were selected
Engineering & Technology / UG
Niva research instrument
12
Participants
IDs 002–013
×
2
Conditions
BF + ST
Preferred speed (W1)
×
2
Feet
Left + Right
×
12
Steps
Per foot / condition
=
576
Selected steps
Eligibility first
No source quality flags.
Finite, nonnegative pressure.
Nonempty, uncut footprint.
retain
Chronological selection
Take the first 12 eligible steps
for each side and condition.
Do not exclude low coverage.
check
Paired quotas
Require both feet.
All quotas met in the
reported subset.
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285. Administrative subset, not a powered population sample. W1 is preferred walking speed. Flags Exclude, Incomplete, Standing and Outlier must all be zero. Verify metadata identity, side, finite nonnegative arrays, nonempty footprints and no boundary contact. Order by StartFrame and FootstepID. Never exclude low coverage or zero sparse signal. No new participant recruitment for R2.

## Slide 8
NIVA / AAVISHKAR 2026–27
08
MAIN RESULTS / FOUR-SENSOR MODEL
Most loaded area remains unobserved
Engineering & Technology / UG
Niva research instrument
3.55%
2.18%
Barefoot (BF)
Sneaker (ST)
Mean loaded area inside the four model discs
Four-sensor model | Barefoot | Sneaker
Participant range, area (%) | 2.76–4.25 | 1.66–2.81
Mean observed load (%) | 3.90 | 2.09
Sparse samples leave most of the reference field without direct measurement.
Means of 12 participant summaries. Ranges are participant minima–maxima, not confidence intervals.
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285. Geometry-derived overlap, not measured Niva accuracy. BF is foot/sock-to-floor, ST is outsole-to-floor; neither is an in-shoe reference. Missing area does not by itself quantify gait-event timing error. Values and participant ranges come directly from archived summary.json.

## Slide 9
NIVA / AAVISHKAR 2026–27
09
RESULTS & COMPARISON
Layout comparison with participant variability
Engineering & Technology / UG
Niva research instrument
Mean loaded area observed (%)
Chart: 
| 4 | 6 | 8 | 13 | 16
Barefoot (BF) | 3.5493 | 5.0317 | 6.0573 | 8.9903 | 11.617
Sneaker (ST) | 2.1811 | 3.2992 | 3.8341 | 6.1136 | 8.2018
Sensor count in each layout model
Participant range, area (%)
Count | BF | ST
4 | 2.76–4.25 | 1.66–2.81
6 | 4.25–5.69 | 2.69–4.02
8 | 4.91–6.51 | 3.08–4.53
13 | 6.95–10.43 | 5.20–7.14
16 | 10.12–13.66 | 6.96–9.62
12 participant means per condition.
Ranges are not confidence intervals.
Count and position both change. The chart compares layouts, not a sensor-count effect.
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285. Native chart stores group means at six decimal places. Native range table uses archived participant minima and maxima, rounded to two decimals. No inference intervals or hypothesis tests were predeclared. All layouts are assumptions, not measured Niva geometry or verified reproductions of published arrays.

## Slide 10
NIVA / AAVISHKAR 2026–27
10
APPLICATIONS & LIMITATIONS
What the study establishes
Engineering & Technology / UG
Niva research instrument
ESTABLISHES
A reproducible coverage benchmark
Quantifies spatial blind area for fixed layouts
on a declared pressure-data subset.
A basis for measurement decisions
Shows where whole-foot interpretations need
additional validation.
DOES NOT ESTABLISH
In-shoe performance
Next: measured geometry and an in-shoe
reference.
Sensor endurance or gate accuracy
Next: R1 cyclic loading, followed by R3 drift tests.
A minimum sensor count
Next: a controlled placement study with declared
error targets.
BF and ST are floor-interface data. No clinical conclusions follow from this study.
Notes: R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285. BF measures foot/sock-to-floor and ST outsole-to-floor pressure. Neither validates in-shoe load distribution, and no conservative lower-bound transfer claim is supported. Future tests listed here are proposed, not completed or newly executed. No clinical inference.

## Slide 11
NIVA / AAVISHKAR 2026–27
11
CONCLUSION & FUTURE SCOPE
Spatial coverage is limited under this protocol
Engineering & Technology / UG
Niva research instrument
The four-sensor model leaves most of the loaded reference
surface outside its active footprints.
R1 / endurance
Cyclic loading and repeated calibration
Sensitivity change: to be measured
R3 / validity
Use aged sensors from R1 to test the gate
Detection performance: to be measured
Next prerequisite: integrate and verify the acquisition fixes before hardware measurement.
Notes: Research framework §7 and firmware defects in Niva_Work_Package.docx. R1 planned fixture1Hz and10,000cycles, not yet measured. R2 subset: run_20260912T161228Z, predeclared protocol 799f322. StepUP-P150: doi:10.20383/103.01285.

## Slide 12
NIVA / AAVISHKAR 2026–27
12
REFERENCES
Sources and reproducibility
Engineering & Technology / UG
Niva research instrument
01
Larracy et al. StepUP-P150 dataset paper
Scientific Data 12, 1415 (2025). doi:10.1038/s41597-025-05792-1
02
StepUP-P150 research dataset
Federated Research Data Repository. doi:10.20383/103.01285
03
Niva predeclared R2 sampling plan
docs/R2_sampling_plan.md · commit 799f322
04
R2 analysis and outcome archive
tools/r2_study.py · docs/r2/run_20260912T161228Z/
05
Niva research framework and work package
Project documents: methods, claims, hazards and planned experiments
Notes: Dataset and authors code attribution: UNB-StepUP/StepUP-P150, pinned ff40d580779bf0ff78b6d5c4d7d183110f02b41a. Dataset CC BY4.0. IBM Plex fonts under OFL, supplied with generator.

## Slide 13
Thank you
Questions & discussion
Observability limits. Endurance testing. Validity reporting.
Notes: No additional result claims.
Niva compact logo vector trace from user-supplied 03_compact_lockup_on_light.png. Transparent flat-colour adaptation, with outlined lettering and a light wordmark on the dark closing slide.